## Slide 1: SN Tool Introduce
2013/07/17
Presenter (Wenping Liu)
Department (ACS7/ST)

## Slide 2: Agenda
SN write option introduce
  Barcode、IMEI、BT Address、Wifi Mac Address
  SN Tool special setting
New SN Tool UI
  SN Tool new main panel
  New UI Modify Item
    Add Login Identify :
      Engineer mode
      Operator mode
    Add Head check mechanism
    Move some select option to menu
    New scan data dialog
SN Tool write procedure example
How to debug when write fail

## Slide 3: SN write option introduce

## Slide 4: SN write option introduce
Barcode
  Production Serial Number for a PCBA, is usually use to identify PCBA. Each
  PCBA should have a barcode number to keep the its test item in production line.
  Barcode should be write to PCBA after download and before ATE calibration,
  because in the calibration station, ATE Tool will write Calibration flag and NSFT
  flag to barcode. If you rewrite use SN Tool, these flags will be cover.
  Support max 64 characters, composed of letters and numbers.
IMEI
  International Mobile Equipment Identity, is a number unique to every GSM and WCDMA phone.
  Must be 15 decimal digits, 14 decimal digits + 1 checksum digit.
BT Address
  Must be 12 characters, composed of letters and numbers.
Wifi Mac Address
  Must be 12 characters, composed of letters and numbers

## Slide 5: SN write option introduce - Special setting
SN Tool Menu - Option
  Mode select
    META mode
      Target will enter META mode to write Barcode、IMEI、BT、Wifi
      Need select correct database file
      Support all Feature Phone 、Smart Phone and Datacard product
    AT mode
      Target will normal bootup and use AT cmd to write Barcode、IMEI、BT、Wifi
      Don`t need select database file
      Current only support feature phone to write barcode、IMEI
  FeaturePhone Option/AT_SDS
    AT mode and want to trigger backup data to SDS, you need select this option
  Datacard
    For Datacard product, enable USBSwitchTool
  External Modem
    For DualTalk project, enable preloader comPort switch to single comPort
  SP Security USB
    For Smart Phone security chip

## Slide 6: SN write option introduce - Special setting
  SN Tool Menu - BT&IMEI
  Lock IMEI
    if check the Lock IMEI, this mean the IMEI can only write one time when current operator is successfully. If you want to rewrite IMEI again, you must Format FAT!!!
If platform is MT6582 smart phone, you should modify such items in SN_SETUP.txt
  World Phone MD Index = 1
  World Phone SW Version = 3 or 5 (3: WCDMA phone; 5 :TD phone)

## Slide 7: New SN Tool UI

## Slide 8: New SN Tool UI - new main panel
Old SN Tool
New SN Tool

## Slide 9: New SN Tool UI - Modify Item
Add menu – “Identify”
  Engineer : Login in engineer mode
    Can Modify UI configuration
    Switch To operator don`t need password
  Operator : Login in operator mode
    No authority modify UI configuration
    Switch to engineer mode need password
Add button – “System Config”
  Setup write barcode、IMEI、BT、wifi option
  Setup the database files
Move some select option to menu
  AT or Meta mode select  ‘ Option’
  Hdcp、DRMKey file select  ‘ Hdcp&Drmkey’
  Datacard、External Modem、SP Security USB  ‘Option’

## Slide 10: New UI Modify Item - Engineer Mode
Engineer Mode
  Engineer mode use for setup all write option, such as select database file, config
  head check string. The mode is the default login mode, The default password is ‘0000’.
  Use the Menu – ’Identity->Engineer->SwitchToOperator’ to switch to operator
  mode, don`t password.
  Use the Menu – ’Identity-> Engineer-> ChangePasswd’ to Modify the engineer password.

## Slide 11: New UI Modify Item - Operator Mode
  Operator Mode
  Operator mode have no authority
  modify UI config. This mode only have
  select comPort num、click Quit and
  Start button authority.
  Use menu -
  ‘Identify->Operator->SwitchToEngineer’
  When switch to engineer mode,
  need input the engineer password.

## Slide 12: New UI Modify Item - Head check mechanism
Function Select
  The option is about
  which type data will be write to
  target at one time. For example,
  if you select IMEI&BT, you can
  write IMEI and BT address to
  target at one time.
  Header Option
  This is when you want to check
  the scan data is valid or not, you
  can turn on the header check. Ex,
  if the wifi address previous 3bits must
  “123”, you can turn on check BT
  address header, and configuration
  the header BT address string is “123”.

## Slide 13: New UI Modify Item - Scan Dialog
Scan Data
  Enable the edit control option base on
  what do you select in the configuration panel.
  If Header check is turn on, the corresponding
  header string will show on edit control tail.
  The current scan data will be highlight.
  The edit control will be disabled when
  scan data finish and header check pass.
  When finish scan all data and click ‘OK’,
  tool will check all data is valid or not. If the
  data is invalid, corresponding edit control
  will be highlight.
  When finish one write flow, this panel
  will be show again.

## Slide 14: SN Tool write procedure example

## Slide 15: SN Write Example - Barcode & IMEI(META Mode)
1、select comPort – UART or USB VCOM
2、select target type – FP/SP/Rndis Dongle/…
3、select write mode – MEAT mode /AT mode
4、click ‘operator config’ button
5、Function select – choose Barcode&IMEI
6、Header option – if check data, turn it on
7、select correct database
8、Click ‘Start’ to scan data
9、Insert cable make phone enter ‘META mode’
10、If Write Result Indicator turn
- Green mean write success
- Red mead write fail
5
6
8
3
10
4
2
1
9
Enter
Meta
mode

## Slide 16: SN Write Example - Barc/IMEI/BT/Wifi(META Mode)
1、select comPort – UART or USB VCOM
2、select target type – FP/SP/Rndis Dongle/…
3、select write mode – MEAT mode /AT mode
4、click ‘operator config’ button
5、Function select – choose Barc/IMEI/BT/Wifi
6、Header option – if check data, turn it on
7、select correct database
8、Click ‘Start’ to scan data
9、Insert cable make phone enter ‘META mode’
10、If Write Result Indicator turn
- Green mean write success
- Red mead write fail
5
6
8
3
10
4
2
1
9
Phone
Enter
Meta
mode

## Slide 17: SN 写号示范 - IMEI/BT(META Mode)
1、选择 端口类型 – UART 或者 USB VCOM
2、选择 手机类型 – FP/SP/Rndis Dongle/…
3、选择 写号模式 – MEAT mode /AT mode
4、点击‘系统配置’ 按钮
5、写号类型选项 – 选择写 IMEI+BT
6、头部检测功能选项 – 需要检测数据正确性, 打开对应的选项
7、选择正确的Database文件
8、点击’开始’按钮扫描数据
9、插入USB或UART数据线，让手机进入META模式
10、如果写操作结果指示器变成
- 绿色表示写操作成功
- 红色表示写操作失败
5
6
8
3
10
4
2
1
9
手机开机进META 模式

## Slide 18: How to debug when write fail

## Slide 19
1、What can I analyse when the operator fail? -- Actually all operator log information display on the main UI
2、If you want to get help from MTK, what information should I offer? -- As the No.1 refer , you can provide the UI Log and the META_DLL.log file, and the META_DLL.log file path default is “C:\”; If Smart Phone, SPMETA_DLL.log also need.