## Slide 1: SN Tool Introduce
2017/11/20
Presenter (Wenping Liu)
Department (ACS7/ST)

## Slide 2: Outline
SN Tool UI
  SN Tool construction
    SN Tool overview
    SN Tool menu
    SN Tool system config panel
    SN Tool scan data dialog
  SN Tool special setting for different product
  SN Tool Engineer & Operator mode
SN Tool write S/N code introduce
  Barcode、IMEI、BT Address、Wi-Fi Mac Address、Hdcp & Drm key
SN Tool write operation procedure
  Preparation
  SN tool setup
  Write examples
    Feature phone write barcode & imei in meta mode via usb cable
    Smart phone write barcode、imei、bt、wifi address in meta mode via uart cable
    Tablet wifi only(without modem) write barcode、wifi address in meta mode via usb
    Tablet wifi only(without modem) install Hdcp data in meta mode by usb
    Rndis Dongle write barcode in meta mode via usb
How to debug when write fail

## Slide 3: SN write UI

## Slide 4: SN Tool overview
The mediatek SN Writer tool is used to write S/N code for a target in META mode, which list below:
  Barcode、IMEI、BT Address、Wi-Fi Address、DRM Key、Hdcp Key
Operate process
Operate message
Popup System configuration panel
Product type
SN Menu

## Slide 5: SN Tool menu
File
  FP Auth File:
    feature phone security project auth file
  SP Auth File:
    smart phone security project auth file
Option
  Already in Meta Mode
    device has already in meta mode, would bypass
    preloader handshake
    only for smartphone or tablet
  Operate Mode
    Meta Mode: target enter meta mode set target S/N
    AT Mode: send AT cmd to set target S/N in normal boot up, current not support yet
  USB Switch Tool
    For dongle product, enable usb swithtool
  External Modem
    For dual talk(external modem) project, enable preloader comport switch to single comport
  Security USB
    For security project

## Slide 6: SN Tool menu
Option
  Security USB
    For security project
  USB Without Battery
    For feature phone product, enable without battery enter meta mode
  Check Flag
    Check Calibration Flag: enable check calibration flag status
    Check NSFT Flag: enable check final test flag status

## Slide 7: SN Tool menu
Hdcp_DRMKey
  Referance “SN Tool write S/N code introduce”
  section for detail
Identify
  Engineer
    Switch to operator: switch to operator mode , disable UI configuration authority
    Change Passwd: change engineer mode passwd
    Enable AutoGen: enable S/N data auto gen feature
  Operator
    Switch to engineer: switch to engineer mode, enable UI configuration authority
Help
  SN Writer tool version information

## Slide 8: SN Tool system config panel (1/2)
Write Option
  The option is about which type data
  will be write to target at one time. Ex,
  if select IMEI&BT, you can write IMEI
  and BT address to target at one time.
  Header Option
  If want to check the scan data
  is valid or not, turn on the header check.
  Ex, if barcode previous 4bits must “1234”,
  turn on check barcode header, and
  configuration the barcode header string
  is “1234”.
  IMEI Option
  IMEI special option
  The number of IMEI was the number of SIM Card Slots

## Slide 9: SN Tool system config panel (2/2)
  DataBase File
  Select ap & modem database files
  If "Load Modem DB from DUT" was checked, tool will try to get mddb file from devices; If try failed, tool will use the db file configed in this UI.
  Log Dir
  Select the directory where all the log will be placed in, and has a sub-directory named by starting date-time.
  Default dir was "C:\SNWriter_LOG"

## Slide 10: SN Tool scan data dialog
Scan Data
  Enable the edit control option base on
  what do you select in the configuration panel.
  If Header check is turn on, the corresponding
  header string will show on edit control tail.
  The current scan data will be highlight.
  The edit control don`t need scan again when
  scan data finish and header check pass.
  When finish scan all data and click ‘OK’,
  tool will check all data is valid or not. If the
  data is invalid, corresponding edit control
  will be empty.
  When finish one write flow, this panel
  will be show again.

## Slide 11: Special setting for different product
  Menu – Option
  USB SwitchTool
    For dongle product, enable usb switchtool
  External Modem
    For dual talk(external modem) project, enable
    preloader comport switch to single comport
    Ex, MT8135(AP) + MT6280(Modem) project
  Security USB
    For security project
  Usb Without Battery
    For feature phone, enable without battery enter meta mode
  System Config – IMEI Option
  IMEI CheckSum
    Enable IMEI checksum mechanism, the last IMEI bit will be
    calculate and replace last bit get from UI
  IMEI Lock
    Lock IMEI, mean the IMEI can only write one time
  DualIMEI Same
    The second imei the same with first imei, don`t need scan imei two times

## Slide 12: SN Tool Engineer & Operator mode
  Engineer
  Have authority to modify UI configuration
  Login in Engineer mode need verify password
  The password default is ‘0000’, use ‘Change Passwd’
  to modify engineer password.
  Switch to Operator mode don`t need password
  Operator
  Have no authority to modify UI configuration
  Switch to Engineer mode need to verify password

## Slide 13: SN Tool write S/N code introduce

## Slide 14: Barcode、IMEI、BT Address 、Wi-Fi Mac Address
Barcode
  Production Serial Number for a PCBA, is usually use to identify PCBA. Each
  PCBA should have a barcode number to keep the its test item in production line.
  Barcode should be write to PCBA after download and before ATE calibration,
  because in the calibration station, ATE Tool will write Calibration flag and NSFT
  flag to barcode.
  Support max 64 characters, composed of letters and numbers.
IMEI
  International Mobile Equipment Identity, a unique number to distinguish
  each mobile phone.
  Must be 15 decimal digits, 14 decimal digits + 1 checksum digit.
BT Address
  Must be 12 characters, composed of letters(a - f or A - F) and numbers.
Wi-Fi Mac Address
  Must be 12 characters, composed of letters(a - f or A - F) and numbers.

## Slide 15: Hdcp & Drm key
8389+8193 Hdcp Key
  For MT8389+8193 project writting hdcp key only .
  Since Writting to nvram , need ap database.
MTK HDCP_DRM Key
  For MTK solution to write hdcp or drm key
Install Hdcp Data
  For vendor to install hdcp data
  this file size must be 572Bytes
  this file size must be 16Bytes
Attestation Key
  Google implement a key file from Android O

## Slide 16: SN write operation procedure

## Slide 17: Preparation
To use the mediatek SN Writer Tool, the following should be preparation:
  Mediatek product that already download MAUI、Moly or APLS software
  UART or USB cable
  S/N code scanner
  Corresponding ap & modem database files
  Make sure the product be power off status

## Slide 18: SN tool setup
Select comPort
  If use uart cable, you should be insert your uart cable
  before launch SN tool, otherwise SN tool can`t show the
  corresponding comport number in the ‘comPort’ ComboBox
Select Target Type
  Feature Phone、Smart Phone、SP DualModem、
  Tablet Wifi Only(without modem)、Rndis Dongle
  MT6276M、MT6280 traditional dongle should be select feature phone
  Dual Talk(external modem, ex. MT8135+MT6280) project, write modem side barcode、imei should be select feature phone, write AP side bt、wifi address should be select Smart Phone
Select operation mode
  Menu->Option->Operate Mode->Meta mode
Click System Config to setup write operation
  Setup write option、select corresponding ap & modem database files
Click Start button to scan S/N code and write to target
1
2
4
3
5

## Slide 19: Feature phone barcode & imei
1、select ComPort – USB VCOM
2、select Target Type – Feature Phone
3、select write mode – MEAT mode
4、click ‘System Config’ button
5、Write Option – choose Barcode & IMEI
6、Header Option – if check data, turn it on
7、select correct modem database files
8、Click ‘Start’ to scan data
9、Insert usb cable make target enter meta mode
10、If Write Result Indicator turn
- Green mean write success
- Red mean write fail
5
6
8
3
4
2
1
9
Enter
Meta
mode
10
7

## Slide 20: Smart Phone barcode、imei、bt、wifi and MEID
1、select ComPort – COM16(UART Cable)
USB VCOM for USB Cable
2、select Target Type –Smart Phone
3、click ‘System Config’ button
4、Write Option – choose Barc/IMEI/BT/Wi-Fi/MEID
5、Header option – if check data, turn it on
6、select correct ap & modem database files
7、Click ‘Start’ to scan data
8、Press power key make target enter meta mode
9、If Write Result Indicator turn
- Green mean write success
- Red mean write fail
7
9
8
Enter
Meta
mode
1
2
3
4
5
6

## Slide 21: Tablet wifi only(without modem) write barc、wifi address
1、选择 端口类型 – USB VCOM
2、选择 手机类型 – Tablet Wifi Only
3、选择 写号模式 – MEAT mode
4、点击‘系统配置’ 按钮
5、写号类型选项 – 选择写 Barcode & Wifi Address
6、头部检测功能选项 – 需要检测数据正确性, 勾选‘On/Off’按钮
7、选择正确的AP Database文件
8、点击’开始’按钮输入或扫描正确的数据
9、插入USB数据线即可，让平板进入META模式
10、如果写操作结果指示器变成
- 绿色表示写操作成功
- 红色表示写操作失败
9
手机开机进META 模式
3
4
2
1
10
8
5
6
7

## Slide 22: Tablet wifi only(without modem) install DRM Key
1、Select ComPort – USB VCOM
2、Select Target Type – Tablet Wifi Only
3、Click menu item MTK HDCP_DRM Key
4、Click DRMKey_File, select a key folder
5、Click ‘Start’ to write key
6、Insert USB cable, make tablet enter meta mode
7、If Write Result Indicator turn
- Green mean write success
- Red mean write fail
Note
If exist a "Recycle" folder in
the key folder, the key file have
been used will be moved to
"Recycle" folder.
7
Target will enter META mode
3
6
5
4
2
1

## Slide 23: Rndis Dongle write barcode
1、select ComPort – USB VCOM
2、select Target Type – Rndis Dongle
3、select write mode – MEAT mode
4、select USB SwitchTool to enable USBSwitchTool
5、click ‘System Config’ button
6、Write Option – choose Barcode
7、Header option – if check data, turn it on
8、select correct ap & modem database files
9、Click ‘Start’ to scan data
10、Press power key make target enter meta mode
11、If Write Result Indicator turn
- Green mean write success
- Red mean write fail
4
6
9
3
11
5
2
1
Enter
Meta
mode
7
8
10

## Slide 24: Install Attestation Key
1、Select ComPort – USB VCOM
2、Select Target Type – Smart Phone
3、Click menu item Attestation Key
4、Click Attestation Key, select a key file, then click "OK" button
5、Click ‘Start’ to write key
6、Insert USB cable, make tablet enter meta mode
7、If Write Result Indicator turn
- Green mean write success
- Red mean write fail
7
Target will enter META mode
3
6
5
4
2
1

## Slide 25: How to debug when write fail

## Slide 26
1、How to debug when the operator fail? -- All operator log information record in "Log Dir" configed in "System Config" Dialog
2、Modem Log
  -- begin support on version > v1.1648.00
  -- setup step
    1. close sn writer, open "SN_Setup.ini" in the exe folder
    2. modify config item "ModemLog" value to "True", save and close "SN_Setup.ini"
    3. put filter file "*.bin" in the exe folder. note: should only one *.bin file in the folder
    4. open sn writer, repeate the issue, modem log will be located in subdirectory of "Log Dir"
3、If you want to get help from MTK, what information should I provide? -- As the No.1 refer , you can provide all the files in subdirectory of "Log Dir".